## Slide 1: Overview Master’s Thesis
Julian Bogenberger 06.11.2023
Automated Steering Measurement

## Slide 2: Overview Past
What has been done?
Sensor Evaluation
External Camera Implementation
  Template Matching
  Edge Detection
  Colored markers for measurement on steering
  Neuronal Network training
  YoloV8 detection
  YoloV8 semantic segmentation
  Angle measurement in 2D

## Slide 3: Overview Past
Sensor Evaluation

## Slide 4: Overview Past
Template Matching
Give system template of features of steering
Scan image for templates
Find enough features to ensure steering position

## Slide 5: Overview Past
Edge Detection
Detect edges in image
Look for features that certain steering is always showing
No measurement so far

## Slide 6: Overview Past
Colored markers on steering
Add markers to steering on 9, 12 and 3 o’clock
Find every mark and connect them
Measure angle (currently only in 2D image plane)
White line represents 0°
Number represents angle of steering

## Slide 7: Overview Past
Neuronal network training
YoloV8 does not support steering wheel class out of the box
Custom training needed
Training for detection task with public dataset
Training for semantic segmentation tasks with custom dataset (Very little dataset)

## Slide 8: Overview Past
Yolo Detection
Detection results in 2D bounding box
Nearly no use for measurements
But representable for class learning
Confidence Score and detection under non-optimal conditions

## Slide 9: Overview Past
Yolo Semantic Segmentation
Detect every pixel that contains steering
May be useful for measurements
Higher error rate than detection
Re-training fixes error (Active Learning)
Misclassification

## Slide 10: Overview Past
Yolo Semantic Segmentation II
After re-training
May be applicable to production environment
  Test-bench fixed and static env
  Manageable quantity of steering variations
!Risk of overfitting!

## Slide 11: Overview Past
Angle Measurement in 2D
Angle is not converted!
Measurement in 2D image plane -> error through camera distortion etc.

## Slide 12: Overview ToDo
What needs to be done?
Timeline
Define precision goals
Test-bench review
External camera view through driver window
Interieur camera Evaluation -> Processing / Measurement
LiDAR usage -> Processing / Detection of steering / Measurement
3D mapping of steering
3D measurements
Self-Calibration -> In-between measurements -> On-site with markers in environment